## Slide 1: Lecture 07: 8255 PPI Chip

## Slide 2
Reference Book:
The 80x86 IBM PC and Compatible Computers
Chapter 11.4
8255 PPI Chip
PPI: Programmable Parallel Interface (so it is an I/O module)

## Slide 3: Recall in Lecture 02: I/O Module Diagram
Data Register
Status/Control Register
External
Device
Interface
Logic
External
Device
Interface
Logic
Input
Output
Logic
Data
Lines
Address
Lines
control
Lines
Data
Status
Control
Data
Status
Control
Systems Bus Interface
External Device Interface

## Slide 4: Package & Internal Structure

## Slide 5: Internal Structure and Pins
Three data ports: A, B, and C
  Port A (PA0~PA7): can be programmed all as input/output
  Port B (PB0~PB7): can be programmed all as input/output
  Port C (PC0~PC7): can be split into two separate parts PCU and PCL; any bit can be programmed individually
Control register (CR)
  Internal register: used to setup the chip
Group A, Group B and control logic
  Group A (PA & PCU)
  Group B (PB & PCL)

## Slide 6: Internal Structure and Pins
Data bus buffer
  An interface between CPU and 8255
  Bidirectional, tri-state, 8-bit
Read/Write control logic
  Internal and external control signals
  RESET: high-active, clear the control register, all ports are set as input port
  ~CS, ~RD, ~WR
  A1, A0: port selection signals
~CS A1 A0 | ~RD ~WR | Function
0 0 0 | 0 1 | PA->Data bus
0 0 1 | 0 1 | PB->Data bus
0 1 0 | 0 1 | PC->Data bus
0 0 0 | 1 0 | Data bus->PA
0 0 1 | 1 0 | Data bus->PB
0 1 0 | 1 0 | Data bus->PC
0 1 1 | 1 0 | Data bus->CR
1 × × | 1 1 | D0~D7 in float

## Slide 7: Operation Modes
Input/output modes
  Mode 0, simple I/O mode:
    PA, PB, PC: PCU{PC4~PC7}, PCL{PC0~PC3}
    No Handshaking: negotiation between two entities before communication
    Each port can be programmed as input/output port
  Mode 1:
    PA, PB can be used as input/output ports with handshaking
    PCU{PC3~PC7}, PCL{PC0~PC2} are used as handshake lines for PA and PB, respectively
  Mode 2:
    Only PA can be used for bidirectional handshake data transfer
    PCU{PC3~PC7} are used as handshake lines for PA
Bit set/reset (BSR) mode
  Only PC can be used as output port
  Each line of PC can be set/reset individually

## Slide 8: Control Register & Op. Modes
Control Register
  A 8-bit internal register in 8255
  Selected when A1=1, A0=1
  Mode selection word
    Input/output modes
    BSR mode

## Slide 9: Select Input/output Modes
Input/output modes
Group A control
Group B control

## Slide 10: Select Input/output Modes
Input/output modes

## Slide 11: Select Input/output Modes
Input/output modes

## Slide 12: Select Input/output Mode Examples
1. Write ASM instructions for setting the 8255 in simple I/O mode with PA and PB being output port and PC being input port.
2. Assume that the address of the control register of the 8255 is 63H, give out the instructions that set up the 8255 in mode 0 where PA, PB and PCU are used as input ports and PCL is used as output port.
MOV AL, 10001001B
MOV DX, ContralPort
OUT DX, AL
MOV AL, 10011010B
OUT 63H, AL

## Slide 13: Select BSR Mode
BSR Mode
Arbitrary value
Indicate which line in PC:
000 – PC0
001 – PC1
…
111 – PC7
0 – Reset
1 – Set

## Slide 14: Select BSR Mode Examples
Assume PC is used as an output port which connects to 8 LED segments, now turn off the second LED segment with the rest unchanged (e.g., for LED segments in this case, 1-on, 0-off).
Using BSR mode instead:
MOV AL, 10000000
OUT ContralPort, AL
…
IN AL, CPORT
AND AL, 11111101B
OUT CPORT, AL
MOV AL, 00000010B
OUT ControlPORT, AL

## Slide 15: Select BSR Mode Examples
Assume the address range for a 8255 is 60H~63H, PC5 is outputting a low level, write code to generate a positive pulse.
MOV AL, 00001011B ; set PC5 high level
OUT 63H, AL
MOV AL, 00001010B ; set PC5 low level
OUT 63H, AL

## Slide 16: Mode 0 (Simple I/O)
For simple input/output scenario
  No handshaking needed
  Any port of PA, PB and PC (PCU, PCL) can be programmed as input or output port independently
  PCU=PC4~PC7, PCL=PC0~PC3
  CPU directly read from or write to a port using IN and OUT instructions
  Input data are not latched, Output data are latched
  E.g., setting up the control register for Mode 0

## Slide 17: Mode 0 Example

## Slide 18: Mode 1 (Strobe I/O)
For handshake input/output scenario
  PA and PB can be used as input or output ports
  PCU=PC3~PC7, used as handshake lines for PA
  PCL=PC0~PC2, used as handshake lines for PB
  Both input and output data are latched

## Slide 19: Mode 1: As Input Ports
PC3~PC5 and PC0~PC2 are used as handshake lines for PA and PB, respectively
  ~STB: the strobe input signal from input device loads data into the port latch
  IBF: Input Buffer Full output signal to the device indicates that the input latch contains information (can also be used for programmed I/O)
  INTR: Interrupt request is an output to CPU that requests an interrupts (for interrupted I/O)
PC6 and PC7 can be used as separate I/O lines for any purpose
INTE: the interrupt enable signal is neither an input nor an output; it is an internal bit programmed via the PC4 (port A) or PC2 (port B); 1-allowed, 0-forbidden

## Slide 20: Mode 1: As Input Ports
Control register
PC stores all status information
Indicates Group A Mode 1
PA: Input
PC6, PC7:
1-input
0-output
Indicates Group B Mode 1
PB: Input

## Slide 21: Timing in Mode 1 Input
Input device first puts data on PA0~PA7, then activates ~STBA, data is latched in Port A;
8255 activates IBFA which indicates the device that the input latch contains information but CPU has not taken it yet. So device cannot send new data until IBFA is cleared;
When IBFA, ~STBA and INTEA are all high, 8255 activates INTRA to inform CPU to take data in PA by interruption;
CPU responds to the interruption and read in data from PA; the ~RD signal will clear INTRA signal;
After CPU finishes reading data from PA (i.e., ~RD signal goes high), the IBFA signal is cleared.

## Slide 22: Mode 1: As Output Ports
PC3, PC6, PC7 and PC0~PC2 are used as handshake lines for PA and PB, respectively
  ~OBF : Output buffer full is an output signal that indicates the data has been latched in the port
  ~ACK : The acknowledge input signal indicates that the external device has taken the data
  INTR: Interrupt request is an output to CPU that requests an interrupts
PC4 and PC5 can be used as separate I/O lines for any purpose
INTE: the interrupt enable signal is neither an input nor an output; it is an internal bit programmed via the PC6 (port A) or PC2 (port B); 1-allowed, 0-forbidden

## Slide 23: Mode 1: As Output Ports
Control register
PC stores all status information
Indicates Group A Mode 1
PA: Output
PC4, PC5:
1-input
0-output
Indicates Group B Mode 1
PB: Output

## Slide 24: Timing in Mode 1 Output
If INTRA active, CPU responds to the interruption and writes data to PA and clears the INTRA signal;
When data has been latched in PA, 8255 activates ~OBFA which informs the output device to pick up data;
After the output device has taken the data, it sends ~ACKA signal to 8255 which indicates that the device has received the data, and also makes ~OBFA go high, indicating CPU can write new data to 8255;
When ~OBFA, ~ACKA and INTEA are all high, 8255 sends an INTRA to inform CPU to write new data to PA by interruption.

## Slide 25: Mode 2 (Bidirectional Bus)
For bidirectional handshake input/output scenario
  Only PA can be used as both input and output port
  PCU=PC3~PC7, used as handshake lines for PA
  Both input and output data are latched

## Slide 26: Mode 2: As Input & Output Port
PC3 ~ PC7 are used as handshake lines for PA
~OBFA, ~ACK, IBFA, ~STBA, INTRA
PC0 ~ PC2 can be used as separate I/O lines for any purpose, or as handshake lines for PB
When CPU responds to an interrupt of 8255 working in Mode 2, the interrupt handler has to check the ~OBFA and IBFA in order to tell whether the input process or the output process is generating the interrupt.

## Slide 27: Mode 2: As Input & Output Port
Control register
PC stores all status information
Indicates Group A Mode 2

## Slide 28: Polling vs. Interruptions
In Mode 1 and 2, PC stores status of Group A and/or Group B
By reading from PC using IN instruction, you can use polling method to check the state of I/O devices

## Slide 29: Programming with 8255
As shown in the figure, PA and PB of the 8255 are working in mode 0. PA used as input port connects to 4 switches, and PB used as output port connects to a 7-segment LED. Write a program to display a hex digit that the switches can represent.

## Slide 31: Address Decoding
What are the addresses of ports and the control register?
PA : 8020H
PB : ?
PC : ?
CR : ?

## Slide 32: A Solution Program

## Slide 33: A Solution Program

## Slide 34: Experiment 2