## Slide 1: Lecture 09: Interrupts & 8259

## Slide 2
Reference Book:
The 80x86 IBM PC and Compatible Computers
Chapter 14
Interrupts and the 8259 Chip

## Slide 3: Interrupts in 8086/8088
256 interrupt types in total
  INT 00 ~ INT 0FFh
Type * 4 = PA of interrupt vector
  The first 1KB is used to store interrupt vectors, called Interrupt Vector Table (IVT)
Interrupt vector points the entrance address of the corresponding interrupt service routine (ISR)

## Slide 4: Main Program and ISR
An ISR is launched by an interrupt event (internal ‘int xx’ or external NMI and INTR) . So ISR is ‘separated’ from main.

## Slide 5: Categories of Interrupts
Hardware (external) interrupts
  Maskable (from INTR)
  Non-maskable (from NMI)
Software (internal) interrupts
  Using the INT instruction
  Predefined conditional (exception) interrupts

## Slide 6: Hardware Interrupts
Non-maskable interrupt
  Trigger: NMI pin, input-signal, rising edge and two-cycle high activate
  TYPE: INT 02
  Not affected by the IF
  Reasons:
    E.g., RAM parity check error, interrupt request from co-CPU 8087

## Slide 7: Hardware Interrupts
Maskable interrupt
  Trigger: INTR pin, input-signal, high active
  TYPE: No predefined type
  IF = 1, enable; IF = 0, disable
    STI sets IF, CLI clears IF
  Reasons:
    Interrupt requests of external I/O devices

## Slide 8: Procedure for Processing Maskable Interrupts
CPU responds to INTR interrupt requests
  External I/O devices send interrupt requests to CPU
  CPU will check INTR pin on the last cycle of an instruction: if the INTR is high and IF = 1, CPU responds to the interrupt request
  CPU sends two negative pluses on the ~INTA pin to the I/O device
  After receiving the second ~INTA, I/O device sends the interrupt type N on the data bus

## Slide 9: Procedure for Processing Maskable Interrupts
CPU executes the ISR of INT N
  CPU reads the N from data bus
  Push the FR in stack
  Clear IF and TF
  Push the CS and IP of the next instruction in stack
  Load the ISR entrance address and moves to the ISR
  At the end of the ISR, IRET will pop IP, CS and FR in turn, CPU returns to previous program and proceeds

## Slide 10: Software Interrupts
INT xx instruction
  An ISR is called upon instruction such as “INT xx”
    E.g., int 21h ; Dos service
  CPU always responds and goes execute the corresponding ISR
    Not affected by the IF
  You can “CALL” any ISR by using the INT instruction

## Slide 11: Difference between INT & CALL
CALL FAR can jump anywhere within 1MB vs. INT jumps to a fix location (finding the corresponding ISR)
CALL FAR is in the sequence of instructions vs. an external interrupt can come in at any time
CALL FAR cannot be masked (disabled) vs. an external interrupt can be masked
CALL FAR saves CS:IP of next instruction vs. INT saves FR + CS:IP of next instruction
last instruction: RETF vs. IRET

## Slide 12: Software Interrupts
Predefined conditional interrupts
  “INT 00” (divide error)
    Reason: dividing a number by zero, or quotient is too large
  “INT 01” (single step)
    If TF = 1, CPU will generates an INT 1 interrupt after executing each instruction for debugging
  “INT 03” (breakpoint)
    When CPU hits the breakpoint set in the program, CPU generates INT 3 interrupt for debugging
  “INT 04” (signed number overflow)
    INTO instruction
    Check the OF after an arithmetic instruction
  ;How to clear TF?
  PUSHF
  POP AX
  AND AX 0FEFFH
  PUSH AX
  POPF
  MOV AX,0009H
  ADD AX,0080H
  INTO

## Slide 13: Procedure for Processing Non-Maskable & Software Interrupts
For NMI
  CPU checks NMI, generates INT 02 interrupt automatically regardless of IF and executes to the ISR
For software (internal) interrupts
  CPU generates INT N interrupt automatically and executes to the corresponding ISR

## Slide 14: Interrupt Vector Table of 8086/8088
5 dedicated interrupts
For system,
27 interrupts
For users,
224 interrupts
256 interrupts
 0～4 dedicated
 5～31reserved for system use
□ 08H～0FH：8259A
□ 10H～1FH：BIOS
 32～255 reserved for users
□ 20H～3FH：DOS
□ 40H～FFH：open

## Slide 15: Interrupt Priority
INT instruction has higher priority than INTR and NMI
NMI has higher priority than INTR
For different external interrupt requests, different strategies can be used to determine their priorities.

## Slide 16: Priority of INTR Interrupts
Software polling
  The sequence of checking determines the priority

## Slide 17: Priority of INTR Interrupts
Hardware checking
  The location in the daisy chain counts

## Slide 18: Priority of INTR Interrupts
Vectored interrupt controller
  E.g., 8259

## Slide 19: 8259
8259 is Programmable Interrupt Controller (PIC)
It is a tool for managing the interrupt requests.
8259 is a very flexible peripheral controller chip:
  PIC can deal with up to 64 interrupt inputs
  interrupts can be masked
  various priority schemes can also programmed.
originally (in PC XT) it is available as a separate IC
Later the functionality of (two PICs) is in the motherboards chipset.
In some of the modern processors, the functionality of the PIC is built in.

## Slide 20: FIGURE 1 Block diagram and pin definitions for the 8259A Programmable Interrupt Controller (PIC). (Courtesy of Intel Corporation.)

## Slide 21: FIGURE 2 All interrupt requests must pass through the PIC’s interrupt request register (IRR) and interrupt mask register (IMR). If put in service, the appropriate bit of the in-service (IS) register is set.

## Slide 22: Interrupt Nesting
Higher priority interrupts can interrupt lower interrupts
:
:
:
:
Main Program
IR2 and IR4 INTR
STI
:
(EOI)
:
IRET
IR2 ISR
STI
:
:
(EOI)
IRET
IR1 ISR
:
STI
:
(EOI)
IRET
IR4 ISR
:
STI
:
:
(EOI)
IRET
IR3 ISR
IR1 INTR
Allow lower priority interrupts
IR3 INTR
Allow lower priority interrupts
Allow lower priority interrupts in 8259
Set IF = 1
Allow lower priority interrupts
IF = 1

## Slide 23: Exp. 3: Interrupts